## Slide 1: 5-BIT ALU
MUHAMMAD USMAN SHAHID (20I-1787)
MUSAAB IMRAN (20I-1794)

## Slide 2: ALU
Arithmetic logic unit (ALU) is a combinational digital circuit that performs arithmetic and bitwise operations on integer binary numbers.
Addition
Multiplication
Division
Subtraction
Comparator

## Slide 3: 5-BIT ALU

## Slide 5: Components
4008 Full Adder
7SEG-COM-CAT-G
XOR
NOR
NAND
AND_3
OR_3

## Slide 6: 5-BIT ADDER

## Slide 7: ADDITION truth table
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1

## Slide 8: ADDITION truth table
Carry-In | A | B | Sum | Carry-Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 9: EXPRESSIONS
SUM = X0R (A, B, Cin).
Carryout = AB +Cin (XOR (A, B))
In the start Cin is given as 0, in start there is no carry in.

## Slide 11: 5-BIT SUBTRACTOR

## Slide 12: 5-BIT MULTIPLIER

## Slide 13: Multiplication truth table
A | B | A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 14: EXPLANATION
It is the AND gate expression, A.B since Multiplication can be done simply by Adding the bits, we will multiply the bits starting from the most significant bit, with all bits of A and then add them by using the adders. For adding we are using the 4-bit adders and making two 4-bit adders to add the 5-bits. The adder will be receiving the 5 bits and three other will be made off and will be adding 5-Bits.

## Slide 15: 5-Bit comparator

## Slide 16: 5-BIT Comparator Truth-TABLE
A | B | A<B | A>B | A==B
0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0

## Slide 17: CIRCUIT DIAGRAM

## Slide 18: Expressions
A==B: (A4’B4 +A4B4’)’. (A3’B3 +A3B3’)’. (A2’B2 +A2B2’)’. (A1’B1 +A1B1’)’. (A0’B0 +A0B0’)’
A<B: (A4’B4) + X4(A3’B3) + X4 X3(A2’B2) + X4 X3X2(A1’B1) + X4 X3X2 X1(A0’B0)
A<B: (A4B4’) + X4(A3B3’) + X4 X3(A2B2’) + X4 X3X2(A1B1’) + X4 X3X2 X1(A0B0’)

## Slide 19: For Equality:
Output y | a |  | b | c | d | e | f | g
0 (not equal) | 1 |  | 1 | 1 | 0 | 1 | 1 | 0
1 (equal) | 1 |  | 0 | 0 | 1 | 1 | 1 | 1
Expressions | 
a, e, f | 1
b, c | Y’
d, g | Y

## Slide 20: For lesser:
Output y equality | Y2 | a | b | c | d | e | f | g
0 (not equal) | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
0 (not equal) | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 (equal) | X | 0 | 0 | 0 | 0 | 0 | 0 | 1
Expressions | 
a, b, | Y’ Y2
g | 1
c, e, f | Y’
d | Y’Y2’

## Slide 21: Greater:
Output y equality | Y2 | a | b | c | d | e | f | g
0 (not equal) | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 (not equal) | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1
1 (equal) | X | 0 | 0 | 0 | 0 | 0 | 0 | 1
Expressions | 
a, b, | Y’Y2’
g | 1
c, e, f | Y’
d | Y’Y2

## Slide 23: Individual contribution
Muhammad Usman Shahid
Comparator
Multiplier
Musaab Imran
Addition
Subtraction

## Slide 24: THANK YOU!